## Slide 1
Vmin Validation Across All Products
CSV output directory: C:\Users\hmarkovi\Downloads\NVLH_Parametric-main\Scripts\parametric-analysis\correlations\.\output\vmin-all-products-validation
Products: NVLHM, NVLHX, NVLPM
Rows in fit summary: 267
Rows in normalized table: 192
Outlier policy:
Vmin: exclude if < 0 or >= 2
UPM: exclude if outside median +/- 3*sigma
Totals from product summary: Accepted=2336930 VminExcluded=5955 UpmExcluded=10210
UPM bounds:
- TPI_UPM::UPM_X_SCREEN_K_START_X_X_X_X_FEM_CALC_UPM_FEM_LVT_FULLDIE_PDK0P9_0950MV_SORT_U1.U2: [0.782, 0.927] N=31214
- UPM_0107_DPMH156P48ULVTINVD4_FULLDIE_0950_MED_SORT_U1.U5: [7610.024, 8420.868] N=31449
- TPI_UPM::UPM_X_SCREEN_K_START_X_X_X_X_FEM_CALC_UPM_FEM_LVT_FULLDIE_PDK0P9_0950MV_SORT_U1.U4: [0.795, 0.924] N=31449

## Slide 2
Top Fits by R2 (Samples >= 20)
Product | Die | Domain | Freq | Core | R2 | N | Vmin@Target
NVLPM | GTDIE | GT | 2.6 | 0 | 0.894 | 2587 | 0.882
NVLPM | GTDIE | GTVPG | 2.6 | 0 | 0.866 | 2587 | 0.843
NVLPM | GTDIE | GT | 2.2 | 0 | 0.845 | 2587 | 0.778
NVLPM | GTDIE | GTVPG | 2.2 | 0 | 0.826 | 2587 | 0.742
NVLPM | HUBDIE | SAPS | 0.75 | 0 | 0.821 | 2639 | 0.823
NVLPM | HUBDIE | SADPU | 2.2 | 0 | 0.821 | 2639 | 0.823
NVLPM | HUBDIE | SAME | 1.2 | 0 | 0.821 | 2639 | 0.823
NVLPM | HUBDIE | SAIOC | 0.75 | 0 | 0.821 | 2639 | 0.823
NVLPM | HUBDIE | SAN | 1.5 | 0 | 0.821 | 2639 | 0.823
NVLPM | HUBDIE | SAVPU | 1.257 | 0 | 0.821 | 2639 | 0.823
NVLPM | HUBDIE | SAC | 2.45 | 0 | 0.821 | 2639 | 0.823
NVLPM | HUBDIE | SAQ | 3 | 0 | 0.821 | 2639 | 0.823
NVLPM | HUBDIE | SACD | 0.787 | 0 | 0.821 | 2639 | 0.823
NVLPM | HUBDIE | SADPU | 2.5 | 0 | 0.785 | 2639 | 0.92
NVLPM | HUBDIE | SAC | 2.7 | 0 | 0.785 | 2639 | 0.92

## Slide 3
Product NVLHM: Normalized Vmin Table
Die | Domain | Freq (GHz) | Vmin
CDIE | AT | 1.2 | 0.473
CDIE | AT | 2.8 | 0.696
CDIE | AT | 3.2 | 0.768
CDIE | AT | 3.6 | 0.857
CDIE | AT | 3.7 | 0.895
CDIE | AT | 3.9 | 0.983
CDIE | AT | 4.2 | 1.065
CDIE | CCF | 1.2 | 0.467
CDIE | CCF | 3 | 0.667
CDIE | CCF | 3.4 | 0.74
CDIE | CCF | 4 | 0.861
CDIE | CCF | 4.3 | 0.971
CDIE | CCF | 4.8 | 1.127
CDIE | CCF | 5 | 1.178
CDIE | CR | 1.2 | 0.482
CDIE | CR | 3 | 0.662
CDIE | CR | 4.1 | 0.858
CDIE | CR | 4.5 | 0.968
CDIE | CR | 4.6 | 1.027
CDIE | CR | 4.8 | 1.056

## Slide 4
Product NVLHX: Normalized Vmin Table
Die | Domain | Freq (GHz) | Vmin
CDIE | AT | 1.2 | 0.477
CDIE | AT | 2.8 | 0.7
CDIE | AT | 3.2 | 0.772
CDIE | AT | 3.6 | 0.86
CDIE | AT | 3.7 | 0.884
CDIE | AT | 3.9 | 1.014
CDIE | AT | 4.2 | 1.063
CDIE | CCF | 1.2 | 0.479
CDIE | CCF | 3 | 0.676
CDIE | CCF | 4 | 0.866
CDIE | CCF | 4.4 | 0.97
CDIE | CCF | 4.6 | 1.06
CDIE | CCF | 4.8 | 1.138
CDIE | CR | 1.2 | 0.483
CDIE | CR | 3 | 0.659
CDIE | CR | 4.1 | 0.855
CDIE | CR | 4.5 | 0.968
CDIE | CR | 4.6 | 1.01
CDIE | CR | 4.8 | 1.084
CDIE | CR | 4.9 | 1.126

## Slide 5
Product NVLPM: Normalized Vmin Table
Die | Domain | Freq (GHz) | Vmin
CDIE | AT | 1.2 | 0.473
CDIE | AT | 2.8 | 0.697
CDIE | AT | 3.2 | 0.77
CDIE | AT | 3.6 | 0.859
CDIE | AT | 3.9 | 0.974
CDIE | AT | 4.2 | 1.078
CDIE | CCF | 1.2 | 0.468
CDIE | CCF | 3 | 0.668
CDIE | CCF | 3.4 | 0.741
CDIE | CCF | 4 | 0.862
CDIE | CCF | 4.3 | 0.967
CDIE | CCF | 4.8 | 1.126
CDIE | CCF | 5 | 1.172
CDIE | CR | 1.2 | 0.483
CDIE | CR | 3 | 0.663
CDIE | CR | 4.1 | 0.855
CDIE | CR | 4.5 | 0.968
CDIE | CR | 4.6 | 0.98
CDIE | CR | 4.8 | 1.059
CDIE | CR | 5 | 1.173